Krownlab, Inc.

2351 NW York St

Portland, OR 97210

Phone:		+1 503-292-6998

Toll Free:		800-356-8586

Fax:		+1 503-206-7236

Website:	www.krownlab.com

E-mail:	sales@krownlab.com

SECTION 08 7123 ‐ SPECIALTY DOOR HARDWARE

Product specification in Construction Specifications Institute (CSi) 3-Part, 2004 MasterFormat

NOTES TO SPECIFIER:

Go to http://www.krownlab.com to verify that this is the most current version of the specifications.

This specification is intended to assist architecture and interior design professionals in the specification of specialty hardware for interior sliding doors using the Construction Specification Institute’s 3-part SectionFormat.

Sample language is provided for articles in Part 1 - General, Part 2 - Products, and Part 3 - Execution.  The sample language, article/ paragraph numbering and overall section format should be edited to fit the design firm’s specifications and the design intent for the project.

Articles and paragraphs of this product specification assume the Project Manual will contain Division 1 General Requirements documents, including close coordination with the following sections as appropriate:

01 2500 “Substitution Procedures”

01 3300 “Submittal Procedures”

01 4300 “Quality Assurance”

01 6200 “Product Options”

01 6600 “Product Storage and Handling Requirements”

01 7400 “Cleaning and Waste Management”

01 7700 “Closeout Procedures”

01 7800 “Closeout Submittals”

If the project manual does not contain these Division 1 sections, appropriate requirements may be provided by the specifier under the appropriate articles within this section.

INSTRUCTIONS:

At paragraphs in blue text, hidden text may be available for guidance in making selections and edits.  The specifier can access the hidden text by selecting on the ¶ symbol within Microsoft Word menus; text will be visible but will remain non-printable unless the font is changed from ‘hidden’ status.  Once selections are made and other options deleted, blue font color should be changed to black.

Optional items requiring selection by the specifier are enclosed within brackets, e.g. “Color:  [white] [black]”.  Once selections are made and other options deleted, blue font color should be changed to black.

AAt paragraphs in green text, LEED requirements are indicated and should be confirmed with the project’s design intent.  These requirements may be deleted if the project is not intended to attain sustainability certification.  Once selections are made and other options deleted, green font color should be changed to black

NOTE:  REMOVE THIS PAGE FROM THE SPECIFICATION SECTION PRIOR TO PUBLISHING CONTRACT DOCUMENTS

Copyright ©2014 Krownlab, Inc.

SECTION 08 7123 ‐ SPECIALTY DOOR HARDWARE

GENERAL

Retain the article below if the Project Manual will contain Division 1 General Requirements documents:

RELATED DOCUMENTS

Drawings and general provisions of the Contract, including General and Supplementary Conditions and Division 01 Specification Sections, apply to this Section.

SUMMARY

Section includes:

Specialty door hardware for sliding doors.

Related Sections:

Retain and/or revise Sections in subparagraphs below that contain requirements Contractor might expect to find in this Section but are specified in other Sections:

Section 062000 "Finish Carpentry" for the provision and installation of wood sliding doors.

Section 064023 "Interior Architectural Woodwork" for the provision and installation of wood sliding doors.

Section 081416 "Flush Wood Doors" for the provision and installation of flush wood sliding doors.

Section 081433 "Stile and Rail Wood Doors” for the provision and installation of stile and rail wood sliding doors.

Section 088000 "Glazing" for the provision and installation of glass sliding doors.

Retain this article if products and work included in this Section are covered by cash or quantity allowance.  It is recommended that, in lieu of the inclusion of allowance amounts at this section, provide a "Door Hardware Allowance" at a Division 1 Section “Allowances” indicating amounts and other requirements.  Insert descriptions of items in this Section at Part 2 or Part 3 to provide information affecting the cost of the Work that is not included under the allowance.

DOOR HARDWARE ALLOWANCE

Furnish door hardware as part of Door Hardware Allowance.

REFERENCES

Retain the articles below if “Bamboo” (Bb) finish is included for BALDUR and/or ODEN lines by Krownlab in this Section:

American Society for Testing and Materials (ASTM):

ASTM E 84 “Standard Test Method for Surface Burning Characteristics of Building Materials.”

Retain the article below if black oxide finish is included in this Section for Black Stainless or Black Steel finishes:

MIL-DTL-13924D “Detail Specification, Coating, Oxide, Black, For Ferrous Metals.”

ACTION SUBMITTALS

Product Data:  For each type of product indicated.  Include construction and installation details, material descriptions, dimensions of individual components and profiles, and finishes.

Sustainability Submittals:

Retain Sections in subparagraphs below that contain requirements necessary to meet the sustainability goals of the project using the preferred sustainability program.

For LEED Credit MR 4, Krownlab products can contribute substantially, containing 42% recycled content in steel and stainless steel components.

Retain the LEED Credit MR 6 when “Bamboo” (Bb) finish is included for BALDUR and/or ODEN lines by Krownlab in this Section.

For Earth Advantage Environmentally Preferable Materials, Krownlab products can contribute for projects within Oregon, and up to two hundred miles distant, including north to Everett, WA, east to Kennewick, WA, southeast to Bend, OR, and south to Roseburg, OR.

USGBC LEED Program:  The requirements of the following LEED credits are mandatory for the work included in this section in order to contribute toward the achievement of LEED certification:

Credit MR 4:  Manufacturers’ product data indicating percentages by weight of post-consumer and pre-consumer recycled content.  Include statement indicating costs for each product having recycled content.

Credit MR 6:  Manufacturers’ product data for products having rapidly renewable content, documentation showing compliance.  Include statement indicating cost for each product having rapidly renewable content.

Shop Drawings:  Include layout of sliding door hardware on sliding doors and relationship to adjoining Work based on field-verified dimensions.

Coordinate locations for contractor-installed blocking within framed walls, by others.

Coordinate locations for contractor-installed anchors at concrete or masonry walls, by others.

Finish Samples:  Provide two (2) finish samples for exposed door hardware of each type required, in each finish specified, prepared on minimum 2-by-2-inch substrate of same base metal.

INFORMATIONAL SUBMITTALS

Qualification Data:  For Installer.

Warranty:  Special warranty specified in this Section.

CLOSEOUT SUBMITTALS

Maintenance Data:  For each type of door hardware, to be included by the General Contractor in the project maintenance manuals.

QUALITY ASSURANCE

Installer Qualifications:  An entity that employs installers who are experienced in door hardware installations that are comparable in material, design, and extent to that indicated for this Project.

WARRANTY

Special Warranty:  Manufacturer's standard form in which manufacturer agrees to repair or replace components of door hardware that fail in materials or workmanship within specified warranty period.

Warranty Period:  Ten (10) years from date of Substantial Completion, unless otherwise indicated.

Exceptions:  Not including normal wear and tear, metal finishes and other consumable materials.

PRODUCTS

PERFORMANCE REQUIREMENTS

Retain "Recycled Content of Steel Products" Paragraph below if required for LEED Credit MR 4.  Krownlab’s steel and stainless steel typically have approximately 40 percent postconsumer recycled content and approximately 2 percent preconsumer recycled content.  Krownlab systems which include bamboo finishes exceed 90 percent postconsumer recycled content (applies to BALDUR and ODEN lines when bamboo (Bb) finish is included).

Recycled Content:

Steel and Stainless Steel Products:  Postconsumer recycled content plus one-half of preconsumer recycled content not less than 25 percent.

Article below applies to BALDUR and ODEN lines when bamboo (Bb) finish is included:

Product Performance Testing:

Article below applies to all product lines by Krownlab in this Section:

Provide products of steel and/or stainless steel construction in which the system has been tested to 130,000 complete cycles using a door panel of 200 pounds weight (exceeding an average of more than 17 complete cycles per day for 20 years; suitable for commercial and hospitality environments).

Retain the article below if “Brushed Stainless” (Ss) finish is included for BALDUR, ODEN and/or ROB ROY lines by Krownlab in this Section:

Provide products of stainless steel construction with No. 4 satin, directional polish finish tested to 130,000 complete cycles using a door panel of 200 pounds weight (exceeding an average of more than 17 complete cycles per day for 20 years; suitable for commercial and hospitality environments).

Provide products of steel construction with black-oxide magnetite (Fe3O4) treatment finish tested to 130,000 complete cycles using a door panel of 200 pounds weight (exceeding an average of more than 17 complete cycles per day for 20 years; suitable for commercial and hospitality environments).

Retain the article below if “Black Stainless” (Bs) finish is included for BALDUR, ODEN and/or ROB ROY lines by Krownlab in this Section:

Retain the article below if “Black Steel” (Bl) finish is included for AXEL line by Krownlab in this Section:

Retain the article below if “Raw Steel” (Rs) finish is included for AXEL line and/or wheel components of ROB ROY line by Krownlab in this Section:

Provide products of steel construction with unfinished treatment tested to 130,000 complete cycles (exceeding an average of more than 17 complete cycles using a door panel of 200 pounds weight per day for 20 years; suitable for commercial and hospitality environments).

Retain the article below if “Bamboo” (Bb) finish is included for BALDUR and/or ODEN lines by Krownlab in this Section:

Retain the article below if “Polished Stainless” (Po) finish is included for BALDUR and/or ODEN lines by Krownlab in this Section:

MATERIALS

Metals:

Retain the article below for steel for AXEL line and/or wheel components of ROB ROY line by Krownlab in this Section.  Retain the article below for stainless steel for BALDUR, ODEN and/or ROB ROY lines by Krownlab in this Section:

Metal Surfaces, General:  Provide metal materials with smooth, flat surfaces, without seam marks, roller marks, rolled trade names, or blemishes.

Steel Plates, Shapes, and Bars:  ASTM A 36.

Stainless-Steel Sheet, Strip, and Plate:  ASTM A 240 or ASTM A 666, Type 304.

Stainless-Steel Shapes and Bars:  ASTM A 276, Type 304.

Stainless-Steel Bars, for Machining:  ASTM A 582, Type 303.

Stainless-Steel Tubing:  ASTM A 554, Grade MT 304.

Stainless Steel Bearing:  SAE 51440C, AISI 440C

Retain the articles below if “Bamboo” (Bb) finish is included for BALDUR and/or ODEN lines by Krownlab in this Section:

MANUFACTURERS

Source Limitations:  Obtain all sliding door hardware from single source from single manufacturer.

Basis-of-Design Sliding Door Hardware Manufacturer:  Krownlab, Inc., Portland, Oregon; www.krownlab.com.

DISTRIBUTORS

Factory Distribution of Basis-of-Design Products:  Krownlab, Inc., Portland, Oregon; www.krownlab.com; sales@krownlab.com; telephone +1 503 292 6998; facsimile +1 503 206 7236.

PRODUCTS

Retain the articles below for inclusion of AXEL hardware in the project; note that top mount and glass systems are not available for AXEL:

Basis-of-Design Sliding Door Hardware:  Provide Axel by Krownlab.

System:  Includes track, two trolleys, two trolley stops, one bottom guide post, track-to-wall mounting hardware, and door-to-trolley mounting hardware.

Material:  Mild steel, except as indicated.

Trolley:  Laser cut from mild steel flat plate; exposed attachment points for face mount door panel.

Door Mounting:  Axel Face Mounting; for door panels 1-3/8 to 1-3/4 inches thick.

Door Mounting:  Axel Top Mounting; for door panels 1-3/8 inches and thicker.

Wheel:  Mild steel 2-25/32 inch O.D. open race bearing.

Track:  1-3/4 x 1/4 inch mild steel laser cut from flat plate; finish as indicated.  Axel track is easily cut and drilled at the project site for field-customization to specific project requirements.

Single-leaf (single track) configuration:  Single 70-inch track is ideal for a 36-inch wide panel with a 32-inch wide door opening, but can be easily modified in the field to accommodate any panel up to 36 inches.  Single 94-inch track is ideal for a 48-inch wide panel with a 44-inch wide door opening, but can be easily modified in the field to accommodate any panel up to 48 inches.  Single 116-inch track is ideal for a 57- to 59-inch wide panel with a 55-inch wide door opening.

Bi-parting (single track) configuration:  Dual 70-inch tracks are ideal for two 34- to 36-inch wide panels with a 66-inch wide door opening, but can be easily modified in the field to accommodate any panels up to 36 inches each.  Dual 94-inch tracks are ideal for two 46- to 48-inch wide panel with a 90-inch wide door opening, but can be easily modified in the field to accommodate any panels up to 48 inches each.  Dual 116-inch tracks are ideal for two 57- to 59-inch wide panels with a 108-inch wide door opening.

AXEL cannot be configured in by-passing (double track) configuration

For AXEL Custom track (minimum quantity of 50 units), indicate the length required, up to 116 inches, or contact the manufacturer for assistance.

Select one of the three articles below for AXEL track length and configuration at single-leaf door openings; delete these articles if a single doors are not used:

Provide a single Axel 70-inch track.

Provide a single Axel 94-inch track.

Provide a single Axel 116-inch track.

Select one of the three articles below for AXEL track length and configuration at double-leaf, bi-parting door openings; delete these articles if bi-parting doors are not used:

Provide two Axel 70-inch tracks for bi-parting (single track) configuration.

Provide two Axel 94-inch tracks for bi-parting (single track) configuration.

Provide two Axel 116-inch tracks for bi-parting (single track) configuration.

Finish:  Manufacturer’s standard finish as follows; refer to Finishes articles:

Select one of the two articles below for AXEL finish; delete other where not applicable:

“Raw Steel” (Rs).

“Black Steel” (Bl).

Capacity:

At single and bi-parting (single) tracks for Axel installations using a single track mount spacer (for thinner panels or glazing and/or without baseboard at wall):  200 lbs. maximum total.

At single and bi-parting (single) tracks for Axel installations using double track mount spacers (for thicker panels and/or with baseboard at wall):  200 lbs. maximum total.

For AXEL custom track (minimum quantity of 50 units), retain the article below.

Customization:  Available; contact:  sales@krownlab.com.

Information:  www.krownlab.com/axel.

Basis-of-Design Sliding Door Hardware:  Provide Axel by Krownlab.

System:  Includes track, two trolleys, two trolley stops, one bottom guide post, track-to-wall mounting hardware, and door-to-trolley mounting hardware.

Material:  Stainless steel, except as indicated.

Trolley:  Laser cut from stainless steel flat plate; exposed attachment points for face mount door panel.

Door Mounting:  Axel Face Mounting; for door panels 1-3/8 to 1-3/4 inches thick.

Door Mounting:  Axel Top Mounting; for door panels 1-3/8 inches and thicker.

Wheel:  Mild steel 2-25/32 inch O.D. open race bearing.

Track:  1-3/4 x 1/4 inch mild steel laser cut from flat plate; finish as indicated.  Axel track is easily cut and drilled at the project site for field-customization to specific project requirements.

Single-leaf (single track) configuration:  Single 70-inch track is ideal for a 36-inch wide panel with a 32-inch wide door opening, but can be easily modified in the field to accommodate any panel up to 36 inches.  Single 94-inch track is ideal for a 48-inch wide panel with a 44-inch wide door opening, but can be easily modified in the field to accommodate any panel up to 48 inches.  Single 116-inch track is ideal for a 57- to 59-inch wide panel with a 55-inch wide door opening.

Bi-parting (single track) configuration:  Dual 70-inch tracks are ideal for two 34- to 36-inch wide panels with a 66-inch wide door opening, but can be easily modified in the field to accommodate any panels up to 36 inches each.  Dual 94-inch tracks are ideal for two 46- to 48-inch wide panel with a 90-inch wide door opening, but can be easily modified in the field to accommodate any panels up to 48 inches each.  Dual 116-inch tracks are ideal for two 57- to 59-inch wide panels with a 108-inch wide door opening.

AXEL cannot be configured in by-passing (double track) configuration

For AXEL Custom track (minimum quantity of 50 units), indicate the length required, up to 116 inches, or contact the manufacturer for assistance.

Select one of the three articles below for AXEL track length and configuration at single-leaf door openings; delete these articles if a single doors are not used:

Provide a single Axel 70-inch track.

Provide a single Axel 94-inch track.

Provide a single Axel 116-inch track.

Select one of the three articles below for AXEL track length and configuration at double-leaf, bi-parting door openings; delete these articles if bi-parting doors are not used:

Provide two Axel 70-inch tracks for bi-parting (single track) configuration.

Provide two Axel 94-inch tracks for bi-parting (single track) configuration.

Provide two Axel 116-inch tracks for bi-parting (single track) configuration.

Finish:  Manufacturer’s standard finish as follows; refer to Finishes articles:

Select one of the two articles below for AXEL finish; delete other where not applicable:

“Stainless Steel” (Ss).

Capacity:

At single and bi-parting (single) tracks for Axel installations using a single track mount spacer (for thinner panels or glazing and/or without baseboard at wall):  200 lbs. maximum total.

At single and bi-parting (single) tracks for Axel installations using double track mount spacers (for thicker panels and/or with baseboard at wall):  200 lbs. maximum total.

For AXEL custom track (minimum quantity of 50 units), retain the article below.

Customization:  Available; contact:  sales@krownlab.com.

Information:  www.krownlab.com/axel.

Retain the articles below for inclusion of BALDUR hardware in the project:

Retain the articles below for inclusion of ODEN hardware in the project:

FABRICATION

Fabrication Tolerances:

Size:

Steel and stainless steel components:  Plus or minus 1/32 inches of required size.

Wood and composite components:  Plus or minus 1/32 inches of required size

All materials, tolerance for length of track and locations of holes in track:  Plus or minus 1/8 inches.

Clearances:  Plus or minus 1/32 inches.

SLIDING DOOR PULLS

Basis-of-Design Sliding Door Pull:  Provide Inger Pull by Krownlab.

Material:  Stainless steel.

Select one of the two items below for RAIL PULL size; custom size available up to 92 inches; indicate on drawings:

Size:  Manufacturer’s standard 2 inch depth by 3/4 inch width by [18-inch length] [47-inch length] [90-inch length] [custom length as indicated, to 90 inches maximum].

Mounting:

Select one of the two articles below for RAIL PULL door panel mounting; delete other where not applicable:

Wood Door Mount; for door panels 3/4 to 3-inches thick.

Select one of the two items below for RAIL PULL door panel configuration; delete other where not applicable:

Configuration:  [Single-sided] [Double-sided].

Finishes:  Manufacturer’s standard finishes as follows; refer to Finishes articles:

Select one of the three articles below for RAIL PULL finish; delete others where not applicable:

“Brushed Stainless” (Ss).

“Black Stainless” (Bs).

Select one of the three colors below for optional RAIL PULL color accent kit:

Select one of the two items below for RING PULL configuration; both RING PULL CLOSED and RING PULL OPEN can be used for solid or glass panels:

Basis-of-Design Sliding Door Pull:  Provide [Ebba Pull Closed] [Ebba Pull Open] by Krownlab.

Material:  Stainless steel; 3/16 inch thickness; Manufacturer’s standard rubber seal at interior face of Ebba Pull Open.

Size:  Manufacturer’s standard 3-1/4 inches diameter.

Mounting:

Select one of the two articles below for RING PULL sizes based on configuration; delete other where not applicable:

At Solid Door Panels:  Manufacturer’s standard 3-1/4 inches O.D., 1-7/8 inches I.D.; for panels 3/4 inch to 3 inches thick.

At Glass Door Panels:  Manufacturer’s standard 3-1/4 inches diameter; for panels 3/8 inch to 3/4 inch thick.

Select one of the two items below for RING PULL door panel configuration; delete other where not applicable.  Note that only Ring Pull Closed for wood can be single-sided. All others must be double-sided:

Configuration:  [Single-sided] [Double-sided].

Finish:  Manufacturer’s standard finish as follows; refer to Finishes articles:

Select one of the three articles below for RING PULL finish; note that “Polished Stainless” (Po) (no. 8 polish) is not recommended for high-use locations, e.g. hotel room bathrooms; delete others where not applicable:

“Polished Stainless” (Po).

“Brushed Stainless” (Ss).

“Black Stainless” (Bs).

ACCESSORIES

Select the BOTTOM GUIDE TRACK for wood doors where routing of the bottom edge of the door to receive the standard bottom guide post is not possible or practical:

Bottom Guide Track:  Manufacturer’s standard bottom guide track to maintain correct wood door alignment through-out the door travel.

Material:  Stainless steel.

Select one of the two items below for BOTTOM GUIDE TRACK finish; delete others where not applicable:

Finish:  [“Brushed Stainless” (Ss)] [Finish:  “Black Stainless” (Bs)].

Select one of the three items below for BOTTOM GUIDE TRACK length; custom length available up to 84 inches; indicate on drawings:

Length:  Manufacturer’s standard [36 inch length] [48 inch length] [Custom length as indicated].

Fastening Hardware:  Stainless steel; included.

Select the TRACK END CAP if desired for BALDUR, ODEN and ROB ROY lines:

Select the DRYWALL SPACER KIT is recommended where heavy or multiple door panels are mounted on drywall; the kit prevents drywall from compressing under the concentrated force at the track attachment to the wall, and help maintain the structural integrity and alignment of the system:

Substrate Spacer:  Drywall Spacer Kit by Krownlab to prevent drywall from compressing under the concentrated force at the track attachment to the wall, and help maintain the structural integrity and alignment of the system.

Material:  Plastic.

Size:  Manufacturer’s standard for 1/2 inch or 5/8 inch gypsum drywall or other substrate.

Finish:  Manufacturer’s standard black color.

Hardware:  Zinc-plated mild steel washers; included.

FINISHES

Retain articles below for all finishes indicated for hardware components:

“Raw Steel” (Rs):  Unfinished/ mill finish steel.

“Black Steel” (Bl):  Steel with a black-oxide magnetite (Fe3O4) treatment in a hot bath of sodium hydroxide, nitrates, and nitrites.  Meet US military specification MIL-DTL-13924, Class 1.

“Stainless Steel” (Ss):  No. 4 satin, directional finish stainless steel.

FASTENERS

General:  Manufacturer shall provide all fasteners for installation of sliding door hardware.  Base metal and finish shall match sliding door hardware.

Steel Bolts and Nuts:  Regular hexagon socket head steel capscrew (or Allen bolt), ASTM A 307, Grade A; and where indicated, with hex nuts, ASTM A 563; and flat washers.

Stainless-Steel Bolts and Nuts:  Regular hexagon socket head stainless steel capscrew (or Allen bolt), ASTM F 593; and where indicated, with hex nuts, ASTM F 594; and flat washers; Alloy Group 1.

If retaining "Anchors, General" Paragraph below, indicate loads on Drawings and verify safety factors with Project's structural engineer.

For Contractor-Installed Anchors:  Contractor shall provide and install anchors capable of sustaining, without failure, a load equal to six times the load imposed when installed in unit masonry and four times the load imposed when installed in concrete, as determined by testing by the manufacturer according to ASTM E 488.

Cast-in-Place Anchors in Concrete:  Either threaded type or wedge type unless otherwise indicated; galvanized ferrous castings, either ASTM A 47 malleable iron or ASTM A 27 cast steel.  Provide bolts, washers, and shims as needed, all hot-dip galvanized per ASTM F 2329.

Post-Installed Anchors:  Torque-controlled expansion anchors or chemical anchors.

Material for mild steel hardware:  Carbon-steel components zinc plated to comply with ASTM B 633 or ASTM F 1941, Class Fe/Zn 5, unless otherwise indicated.

Material for Stainless Steel Hardware:  Alloy Group 1 stainless-steel bolts, ASTM F 593, and nuts, ASTM F 594.

EXECUTION

EXAMINATION

Examine door panels and substrates at the door openings, with the specialty door hardware Installer present, for compliance with requirements for installation tolerances, wall and floor construction, and other conditions affecting installation and performance.

Proceed with installation only after unsatisfactory conditions have been corrected.

PREPARATION

Attachment points for specialty door hardware may not align with existing framing or blocking locations.  Heights and locations for installation of specialty door hardware components are indicated on Drawings.

At wood or light-gauge metal framed partitions, ensure the provision and proper installation of additional framing or blocking within the partition’s framing cavity prior to hardware installation.

Coordinate the correct location for additional blocking or framing; height of the attachment point is based on the overall height of the door panel; the location for track mounting points is approximately 2-1/4 inches above the top of door panel.

Retain either or both of the articles below, as required.

In new construction, ensure appropriate blocking is added in the correct locations during framing, prior to drywall installation.

In renovations, partially remove drywall to expose the framing cavity and install appropriate blocking in the correct locations.

Retain either or both of the articles below, as required.

Wood or Other Solid Panel Doors:  Provide holes and cutouts in glass to receive hardware, fittings, and accessory fittings.  Ensure adequate blocking within the core of the wood or other solid door panel, or comply with DHI WDHS.5 "Recommended Hardware Reinforcement Locations for Mineral Core Wood Flush Doors."

Comply with specialty door hardware manufacturer's written recommendations for locations and other dimensions for holes and cutouts in wood panels.

INSTALLATION

Install each specialty door hardware item to comply with manufacturer's written instructions. Where cutting and fitting are required to install specialty door hardware onto or into surfaces that are later to be painted or finished in another way, protect specialty door hardware items until finishes have been completed on substrates involved.

Set specialty door hardware items level, plumb, and true to line and location. Adjust and reinforce attachment substrates as necessary for proper installation and operation.

Appropriately prepare substrates that are not as indicated for manufacturer-provided anchorage fasteners. Space fasteners and anchors according to manufacturer's written instructions.

At Gypsum Board Drywall Finishes:  Utilize the manufacturer’s standard substrate spacer to prevent drywall from compressing under concentrated forces at the track attachment to the wall, and help maintain the structural integrity and alignment of the hardware system

ADJUSTING

Adjust and check each operating item of door hardware and each door to ensure proper operation or function of every unit. Replace units that cannot be adjusted to operate as intended.

Following installation and adjustment, cycle the door panel open and closed 20 times to redistribute the lubricant within the wheels (bearings).

CLEANING AND PROTECTION

Clean adjacent surfaces soiled by specialty door hardware installation.

Clean operating items as necessary to restore proper function and finish.

Retain either or both of the articles below for finishes indicated for hardware components:

For “Black Steel” (Bl) components:  With a clean towel, apply a thin coating of petroleum jelly (e.g. Vaseline by Unilever:  www.vaseline.us) and buff clean and dry.  Test at an obscure location to confirm acceptability of treatment.

Provide final protection and maintain conditions that ensure that specialty door hardware is without damage or deterioration at time of Substantial Completion.

MAINTENANCE

Wheels (bearings) should occasionally be lubricated with bearing oil (e.g. SHC 630 Synthetic Gear and Bearing Oil by Exxon Mobil Corp.:  www.mobil.com).

END OF SECTION 08 7123

Retain this page as required to allow document to be an even number of pages, for printing reasons within the overall specification book or project manual.

THIS PAGE INTENTIONALLY BLANK